CCS811 connected to Raspberry PI

# 1. CCS811 and Raspberry: A problem with I2C?

You could get a lot of miss readings and errors with the CCS811 connected to a Raspberry PI. The reason is a different intepretation of handling clock stretching. CCS811 is using clock stretching.

## 1.1 What is clock stretching?

According to NXP I2C-bus specification ( https://www.nxp.com/docs/en/user-guide/UM10204.pdf)

Clock stretching pauses a transaction by holding the SCL line LOW. The transaction cannot continue until the line is released HIGH again. Clock stretching is optional and in fact, most slave devices do not include an SCL driver so they are unable to stretch the clock.

On the byte level, a device may be able to receive bytes of data at a fast rate, but needs more time to store a received byte or prepare another byte to be transmitted. Slaves can then hold the SCL line LOW after reception and acknowledgment of a byte to force the master into a wait state until the slave is ready for the next byte transfer in a type of handshake procedure.

On the bit level, a device such as a micro-controller with or without limited hardware for the I2C-bus, can slow down the bus clock by extending each clock LOW period. The speed of any master is adapted to the internal operating rate of this device.

## 1.2 Why does this not work well on the Raspberry Pi

The BCM2835 just does not handle it well.

The SCL line is forced low by either the master or slave and, if released by both, it is pulled high by the pull-up resistors. The master normally provides the on-going clock signal, and so does the BCM2835. It pulls the SCL low for half of the clock cycle and releases for the line to be pulled-up for another half. The time is depending on the clock speed. The data is read from SDA when the SCL signal changes from low to high.

Assume 100Khz, the cycle time is 10us, thus 5us low and 5us high. Clock stretching should be detected by the master when it releases the SCL line. It should detect that the line is staying low (now forced by the slave) and should wait until it is released by the slave. Then it should restart the clock again with the 5us high time.

The BCM2835 does not wait however and seems to let it’s clock running. If the slave releases the line before master clock high-time expires (within the 5us), the SCL line will be pulled-up high and then forced low again when that master clock high-time expires.

If you are lucky, the clock_stretch done by the slave is short enough to leave enough SCL high time for the slave to recognise the clock and stay synchronised. If that high time pulse is too short OR when the slave releases the SCL when the master clock high time has expired and the master has already forced the SCL for the 5us low, the master and slave are out of sync. The result is unpredictable, mostly leading to NACK errors.

This also explains that when you set a lower clock speed, like 35Khz instead of 100Khz, the clock cycle time is now much longer (~32us), leading to 16us high and 16us low. The chance that a slave device releases it’s clock stretch within the master clock high-time has now been increased. But still for some devices that is not enough. E.g. the SCD30 has documented that it can take 14mS.

NOTE : The BCM2835 does have the ability to set a maximum clock stretch limit, but all that does is detect and generate an error if the SCL line stayed low for longer than that period time.

## 1.3 Live example: I2c speed 100Khz
This is performed with a CCS811 from Arduino. The CSS811 is using clock stretch.

A read for data available request is performed on 0x5A, register 0. The responds is 0x98, follow by a stop from the master. As 3 bit is set a next step is to perform a start and a request for the data (0x5a + register 0x02), followed by stop. As this is a multi byte read (as defined in the datasheet), a start + slave address1 read is sent (0x5a) , followed by 2 bytes sent by the slave to the master (2 x zero values). That is repeated for the next 2 bytes (only half of the first of those bytes is seen on the picture).

Zooming In on the same picture, we see slave address 1 + data-byte1 + data byte2

The next level to zoom on the same picture. We see the clock streth happening after sending the slave address. As the clock stretch expires when the master clock (if it would not have been held by clock stretch) would still be high (just), as such a small spike on the SCL. However the CCS811 had not pulsed SDA down yet, but release the clock and set SDA at the same time !

On deeper zoom on the same picture…
The clockstretch is only 9us, way below the default 640us of the BCM2835, but as it expires and the SCL line is released and becomes high, SDA line is not stable yet. Now it is down to luck, nano seconds, whether it read a ‘ 0’ or a ‘1’ from the SDA

Now we zoom out 1 step.. The CCS811 and the Raspberry get out of sync..

We see the clock stretch and now counting the number of bits in red. The CCS811 was expecting a low SCL before a high SCL. So it counts the 8 bits (in red), releases SDA. which should now be pulled down by the master for an ACK. BUT that does not happen. The BCM2835 started counting with the small clock spike immediately following clock stretch release. As such the on the moment where the slave is submitting the 8th bit, the master was also providing the ACK.

Only luck can make this work OR a lower speed.

## 1.4 Let’s try I2C on 35Khz.

Not repeating the whole cycle but starting the moment after sending slave address1 with 35Kz. The cycle time is now ~28us (14 low/14 high).

The clock stretch signal from the slave is NOT exceeded the master clock low time (remember the clock stretch is only 9us as we have seen earlier). Thus the SDA has been pulled down during the low time of the master clock and the CCS811 and BCM2835 stay in sync.

They stay in sync looking at the byte1 and byte 2

## 1.5 Conclusion

The CCS811 and BCM2835 get out of sync due to a different interpretation around handling and restarting AFTER clock stretch. As long as the clock stretch (like 9us) ends within a high period of the master clock there is no problem. This means that the maximum speed should be 55Khz (causing an 9us low/ 9 us high). Actually when running on 70% (35Khz) there is no issue to be found.

This is a known issue with the BCM2835 and as this hardware… you can NOT change it.. you have to run at low speed like 35Khz OR build you own bit banging for I2C.