TwoWire (I2C) library Raspberry Pi

The BCM2835 chip provides I2C communication protocol from the hardware. However the clock stretching implementation is bad, leading to many issues with slave devices that depend on or use clock stretching to handle the requests. (e.g. CCS811, SCD30 ) This library can handle that.

This library for the Raspberry Pi can be instructed to use the standard (hardware) I2C communication OR use a software version that supports clock stretching on any of the GPIO pins. This also supports for you to run multiple I2C channels at the same time on different GPIO. To have low processor load and increase stability, the maximum speed that is supported for the soft_I2C is 200Khz. However for compatibility reasons a higher speed request (max. 400Khz) will be accepted, which can be executed by hardware I2C communication, but for software I2C the maximum executed will be around 200Khz.

software version :
advantage:
can run multiple I2C channels for different programs in parallel
flexible on GPIO’s to use
run as any user (does not need root permission)
supports proper clock-stretch

disadvantage:
generates some process load (although acceptable low)
quality of communication depending on total processor load
supports speeds up to max 200Khz

hardware version :
advantage
generates lower process load
less / no dependency on processor load from other programs
supports speeds up to max 400Khz

disadvantage
single channel
fixed GPIO’s ( 2 and 3)
must be root or super user.
No clock-stretch support

WARNING: Be aware however that software I2C the process load can be of impact on the quality of communication with the slave device.

# 1. Program Structure
This is a high level overview where the twowire API fits compared to the user program, the BCM2835 library and the BCM2835 chip

User program
Soft I2C
twowire API
bcm2835 API
/dev/mem or /dev/kmem
(Depending on user permission)
twowire.h
bcm2835.h

Hard I2C

BCM2835

# 2. Software
## 2. 1 Installation

As with many of my projects I make use of the BCM2835 library to control the IO. This is a library that communicates directly with the BCM2835 hardware, not using the I2C code from the kernel and thus allowing high response speed and flexibility.

### 2.1.1 BCM2835 library
Install latest from BCM2835 from : http://www.airspayce.com/mikem/bcm2835/

1. wget http://www.airspayce.com/mikem/bcm2835/bcm2835-1.56.tar.gz
2. tar -zxf bcm2835-1.56.tar.gz	(1.56 was version at the time of writing)
3. cd bcm2835-1.56
4. ./configure
5. sudo make check
6. sudo make install

In order for this software to run you should NOT enable i2C in raspi-config to load the kernel drivers. It works directly on the hardware, but you’ll have to run program as root.

### 2.1.2 twowire library
Obtain the latest version from : https://github.com/paulvha/twowire

1. download the zip-file (clone or download / download zip-file) in the wanted directory
2. unzip twowire-master.zip (*1)
3. cd twowire-master
4. make install

*1) if you do not have unzip : sudo apt-get install zip unzip

“make install” will create and install a dynamic library,. If needed “make install-static” creates a static library, In the software directory you will find the following files (next to this document)

twowire.cpp :
This is the source of the library that will be discussed in detail in a next section.

twowire.h :
This is the header file for the twowire library.

makefile :
script to compile the source and create an executable with the make command.

### 2.1.3 How to include in program?

To access and compile a user program correctly, add on top in the user program:
# include <twowire.h>

Add when compiling to include both libraries : -ltwowire -lbcm2835

### 2.1.4 examples where library has been used

CCS811 : : https://github.com/paulvha/css811

BM280 : : https://github.com/paulvha/bme280
# 3. TwoWire library API calls

## 3.1 Soft-I2C and Hard_I2C
### 3.1.1 TwoWire(void)
This is the constructor and should be set at the beginning of a user program to create a global constructor to get access to the I2C calls.

Example : TwoWire TWI;
Any next call can be referenced like TWI.begin (..)

### 3.1.2 setDebug(bool db)
Enable (true) or disable (false) messages from the driver. Default is disabled.

### 3.1.3 setPullup()
Enable internal BCM2835 pull-up resistors on the SDA and SCL line. MUST be called BEFORE begin. Some slave devices do NOT have pull-up resistors. You can either add external resistors or use the BCM2835 internal pull-up resistors.

Note 1: GPIO 2 and 3 the Raspberry Pi have hard-wired resistors already and are omitted.

Note 2: The internal BCM2835 resistors are ~10K, while the hardwired resistors are 1K8. External pull-up resistors (~1K for 3V3, ~1K8 for 5V , max- ~4k7) are preferred above internal pull-up for signal quality, especially with longer I2C lines and high speed.
### 3.1.4 begin(bool Itoc, int sda, int scl)
Must be called to set the I2C communicator being used.

Itoc can been hard_I2C or soft_I2C.
If hard_I2C the I2C communication is handled by the BCM2835 chip (hardware). The advantage is little to none dependency on the process load from the programs running. It also provides speed upto 400Khz. The disadvantage is that the clock stretching is very badly handled (read: NOT) by the chip, it is down to luck. The SDA and SCL GPIO info is not used as this is defined by the hardware (GPIO 2 and 3).

If soft_I2C the I2C communication is handled by bit-banging (software). The advantage is full support of clock stretching as well as this can be implemented on any GPIO. Multiple versions can run in parallel, providing additional independent I2C channels. The disadvantage is that it could be impacted by processor load and the maximum speed is 200Khz. The SDA and SCL GPIO are used and these are by default GPIO 2 and 3, but can be changed. SDA and SCL are GPIO numbers. NOT PIN location !

### 3.1.5 setSlave(uint8_t address)
Sets the slave address of the I2C device to communicate with in the next call. Must be set before the read of write communication the I2C slave device.

### 3.1.6 setClock(uint16_t freq)
Will set the I2C timing and clock frequency to use to the device. Between 1 and 400 Khz . By default 100Khz. The hard_I2C can handle up to 400Khz, soft_I2C max 200Khz (even if higher speed is requested)

### 3.1.7 i2c_write(char *buffer, uint8_t length)
Will write an amount of bytes (defined by length) from the buffer to the I2C slave device. It will either use the hardware or software I2C communicator as defined during begin().

### 3.1.8 i2c_read(char *buffer, uint8_t length)
Will read an amount of bytes (defined by length) from the I2C slave device into the buffer. It will either use the hardware or software I2C communicator as defined during begin().

### 3.1.9 i2c_read_rs(char *regaddr, char *buffer, uint8_t length)
Will read an amount of bytes (defined by length) from the register of an I2C slave device into the buffer using restart. This means you first write the slave and register, then perform another start (instead of stop), sent the slave address again for reading and start reading. The slave device has to support this (check the data-sheet). It will either use the hardware or software I2C communicator as defined during begin().

### 3.1.10 close()
Will close the I2C communicator, set the GPIO back to the right state and release memory where applicable.

### 3.1.11 linestatus()
Will check the status of the SDA and SCL line.
Returns :
     I2C_OK : no line error detected
     I2C_SCL_HELD_LOW : SCL line is held low
     I2C_SCL_HELD_LOW_AFTER_READ : SCL is held low for longer than clock stretch
     I2C_SDA_HELD_LOW : SDA line is held low
     I2C_SDA_HELD_LOW_AFTER_INIT : error during I2C start sequence

## 3.2 Soft-I2C only
### 3.2.1 setClockStretchLimit(uint32_t limit)
Will set the maximum Clock Stretch Limit and clear statistics. By default 200us.

### 3.2.2 GetStretchStat(clock_stretch &stat);
Will provide information around clock stretch statistics when running the software I2C. The format is clock_stretch structure as defined in twowire.h. The timing values are in (~us). Due to program overhead and not running in real-time operating environment (as Linux is multi-tasking) the numbers are an indication. Depending on the processor load the numbers are between 5 to 10%
accurate.

It will provide the following statistics since last set limit or cleared :

The limit that was set (default 200),

// while reading from the slave device
maximum amount of stretch count,
minimum stretch count (excluding zero count),
total amount stretch counted,
amount of time clock stretch happened
the number of times the limit was exceeded (err).

// while writing to the slave device
maximum amount of stretch count,
minimum stretch count (excluding zero count),
total amount stretch counted,
amount of time clock stretch happened
the number of times the limit was exceeded (err).

### 3.2.3 ClrStretchStat()
Will clear the stretch statistics for a fresh start.

### 3.2.4 DispClockStretch()
Will display the clock stretch statistics with simple printf() statements. Can be used for diagnoses
### 3.2.5 flush()
Will flush transmit and receive buffers. This is normally handled by the driver, but can be used to clear manually.

# 4. Clock stretching

## 4.1 What is clock Stretching?

According to NXP I2C-bus specification ( https://www.nxp.com/docs/en/user-guide/UM10204.pdf)

Clock stretching pauses a transaction by holding the SCL line LOW. The transaction cannot continue until the line is released HIGH again. Clock stretching is optional and in fact, most slave devices do not include an SCL driver so they are unable to stretch the clock.

On the byte level, a device may be able to receive bytes of data at a fast rate, but needs more time to store a received byte or prepare another byte to be transmitted. Slaves can then hold the SCL line LOW after reception and acknowledgment of a byte to force the master into a wait state until the slave is ready for the next byte transfer in a type of handshake procedure.

On the bit level, a device such as a micro-controller with or without limited hardware for the I2C-bus, can slow down the bus clock by extending each clock LOW period. The speed of any master is adapted to the internal operating rate of this device.

## 4.2 Why does this not work well on the Raspberry Pi

The BCM2835 just does not handle it well.

The SCL line is forced low by either the master or slave and, if released by both, it is pulled high by the pull-up resistors. The master normally provides the on-going clock signal, and so does the BCM2835. It pulls the SCL low for half of the clock cycle and releases for the line to be pulled-up for another half. The time is depending on the clock speed. The data is read from SDA when the SCL signal changes from low to high.

Assume 100Khz, the cycle time is 10us, thus 5us low and 5us high. Clock stretching should be detected by the master when it releases the SCL line. It should detect that the line is staying low (now forced by the slave) and should wait until it is released by the slave. Then it should restart the clock again with the 5us high time.

The BCM2835 does not wait however and seems to let it’s clock running. If the slave releases the line before master clock high-time expires (within the 5us), the SCL line will be pulled-up high and then forced low again when that master clock high-time expires.

If you are lucky, the clock_stretch done by the slave is short enough to leave enough SCL high time for the slave to recognize the clock and stay synchronized. If that high time pulse is too short OR when the slave releases the SCL when the master clock high time has expired and the master has already forced the SCL for the 5us low, the master and slave are out of sync. The result is unpredictable, mostly leading to NACK errors.

This also explains that when you set a lower clock speed, like 35Khz instead of 100Khz, the clock cycle time is now much longer (~32us), leading to 16us high and 16us low. The chance that a slave device releases it’s clock stretch within the master clock high-time has now been increased. But still for some devices that is not enough. E.g. the SCD30 has documented that it can take 14mS.

NOTE : The BCM2835 does have the ability to set a maximum clock stretch limit, but all that does is detect and generate an error if the SCL line stayed low for longer than that period time.
## 4.3 What is the right clock stretch value ?

By default the clock stretch value for soft_I2C is ~200us. Given that Linux is not a real-time operating system, one should expect with 5% accurate. Sometimes the data-sheet will indicate the maximum expected clock stretch, else you can set an unexpected high number ( 200000 =200mS). Now leverage the DispClockStretch() call as in Appendix A .
Run your program and include to display the clock stretch results. The clock-stretch needed can be depending on the commands to be executed by the slave. Perform some different tests and then set the clock stretch for 2 to 3 times the maximum observed. That is a save boundary. In case SCL line is not released within that limit you either have a wiring or device problem.

WARNING: Especially under processor load and when running multiple soft_I2C instances at the same time, you can find a low amount of events and clock-stretch time usage. These might not be caused by the slave device, but just because of multitasking Linux. Best to perform the test as standalone as possible.

## 4.4 My device does not seem to use clock-stretch

There are many slave devices that have not implemented or not use clock stretch and as such there will be no or little clock-stretch reading. Now what ?

Honestly…...up to you…

You can continue to use the same library soft_I2C library. Especially nice if you want to create multiple I2C channels or a single channel but on other GPIO and use GPIO 2 and 3 for something else.

If your slave supports speed more than 200Khz, and you want that, or you want less processor load it might interesting to switch to hard_I2C.

# 5. Example code

## 5.1 General flow

The general program flow will be:

# include <twowire.h>

TwoWire	TWI;	// Create global constructor

main()
{
TWI.pullup();	// optional to enable internal pull-up resistors

TWI.begin(Soft_I2C, 2, 3);	// initialize I2C communication for soft_I2C

TWI.setDebug(true);	// Optional to enable driver messages

TWI.setClock(200);	// Optional overrule default clock (100Khz) to 200Khz

TWI.setClockStretchLimit(1000)	// Optional change default stretch limit(200us) to
   ~1000us

TWI.setSlave(add)	// set I2C slave address

TWI.i2c_write(buf, len)	// write a request to the slave

TWI.i2c_read(buf, len)	// read values from the slave

TWI.close();	// reset hardware and release memory
}

# Appendix A: Sample Code to display the clock stretch statistics

# include <twowire.h>

/* global constructor for I2C (hardware of software) */
TwoWire TWI;

………..…now perform actions like …………………………..

TWI.begin(Soft_I2C, 2, 3);	// initialize I2C communication for soft_I2C. SDA GPIO 2,
  SCL GPIO 3

TWI.setClockStretchLimit(1000)	// Optional overrule default stretch limit(200us) to ~1000us

TWI.setSlave(0x5A)	// set I2C slave address

TWI.i2c_write(buf, len)	// write a request to the slave

TWI.i2c_read(buf, len)	// read values from the slave
………………………………………………………………………….

TWI. DispClockStretch() Output example :

clock_stretch_limit	1000 uS
   max	min	total time	events	errors
   uS	uS	uS	#	#
read 48	37	214	5	0
write 55	37	345	8	0

Clock_stretch :
max : maximum time (uS) observed during read of write
        min : minimum time (uS) observed during read of write (0us is omitted)

limit total time
Total clock_stretch of all events happened

events
total amount of clock-stretch events that happened (0us is omitted)

errors
Total amount of events the clock-stretch limit was reached during read/write